## Slide 1
AIVOA.AI
SECTION 2
Understanding QMS
Workflow
Pharmaceutical Quality Management Systems
in Real-World API & FDF Manufacturing
Real-World Example: Metformin HCl (API) → Metformin 500mg Tablets (FDF)

## Slide 2
What is a Quality Management System (QMS)?
A QMS is a structured framework of processes, procedures, and responsibilities that pharmaceutical manufacturers use to achieve and maintain product quality—ensuring every batch meets regulatory standards (FDA 21 CFR, ICH Q10, GMP).
Deviations
Track & investigate unexpected events in manufacturing
CAPA
Corrective & Preventive Actions to eliminate root causes
Quality Checks
In-process & release testing for every batch
Recalls & Audits
Market withdrawals & periodic system reviews

## Slide 3
Real-World Example
From Raw Material to Patient-Ready Tablet
API — Active Pharmaceutical Ingredient
Metformin Hydrochloride (HCl)
Antidiabetic drug — widely manufactured globally
Produced via chemical synthesis (guanidine + dimethylamine)
Must meet USP/Ph.Eur. purity standards (≥99.0%)
Key tests: Assay, Related substances, Heavy metals, Particle size
→
FDF — Finished Dosage Form
Metformin HCl 500mg Immediate-Release Tablets
Oral solid dosage for Type 2 Diabetes patients
Excipients: Povidone, Magnesium stearate, HPMC
Must meet dissolution (≥80% in 45 min), hardness, uniformity specs
Packaged in HDPE bottles or blister packs

## Slide 4
QMS Lifecycle: Metformin Manufacturing Journey
01
Raw Material
Receipt & Testing
›
02
API Synthesis
& In-Process QC
›
03
FDF Manufacturing
& Granulation
›
04
Final Release
Testing
›
05
Market Distribution
& Surveillance
QMS Modules
Supplier CoA check
Deviation if out-of-spec
Material rejection
QMS Modules
Batch Record review
In-process deviation
Specification check
QMS Modules
Blend uniformity check
Compression monitoring
CAPAs if needed
QMS Modules
CoA generation
QP release sign-off
Lab OOS investigation
QMS Modules
Post-market surveillance
Recall management
Pharmacovigilance

## Slide 5
Deep Dive: Deviation & CAPA Workflow
Scenario: During Metformin tablet compression, 3 tablets in Batch #MT-2024-078 failed hardness specs
DEVIATION REPORT
1
1. Detection:
QC operator flags 3 tablets.
2
2. Immediate Action:
Batch quarantined.
3
3. Documentation:
Deviation raised in QMS. Batch record annotated
4
4. Investigation:
Root cause: punch tooling wear + over-lubrication.
5
5. Impact Assessment:
Retesting of 20 tablets. 17 pass. Batch partially released after QP review
CAPA (Corrective & Preventive Action)
1
Corrective Action:
Replace worn punches.
2
Root Cause Verified:
Test batch confirms hardness— within spec across all tablets
3
Preventive Action:
Add punch wear check every.
4
Training:
Operators retrained on over-lubrication risks. Training records filed in QMS
5
Effectiveness Check:
Next 3 batches monitored. No recurrence in 6-month review. CAPA closed

## Slide 6
How QMS Modules Interconnect — The AIVOA.AI Advantage
QMS
Core
Platform
Deviations
Capture, classify & investigate deviations in real-time
CAPA
Link root causes to actions with effectiveness tracking
Change Control
Manage SOPs, equipment, and process changes
Batch Records
Electronic batch records with e-signature & audit trail
Training & Compliance
Auto-assign training on SOP updates
AIVOA.AI digitizes this entire interconnected QMS ecosystem — replacing paper, email chains, and spreadsheets with intelligent, audit-ready workflows.

## Slide 7
KEY TAKEAWAYS
QMS in Pharmaceutical
Manufacturing
QMS is the backbone of GMP compliance — every deviation, CAPA, and test is documented and traceable.
Deviations and CAPAs are interconnected — a deviation always triggers investigation and potentially a CAPA.
Quality checks happen at every stage: incoming RM, in-process, and final release — not just at the end.
Recalls are rare but critical — QMS provides the traceability needed to act within hours, not days.
AIVOA.AI transforms these manual, paper-heavy workflows into intelligent, connected digital systems.